## Slide 1: Reāltime wireless gaana streaming Final Project Presentation under the guidance of Prof. Kavi Arya
Bharat Reddy, Diptesh Kanojia, and Vinod Saini
CS684: Embedded Systems Project
CSE Department, IIT Bombay
27th October, 2016

## Slide 2
Roadmap
14th September, 2016
Problem Statement
Requirements
Work Allocation & Timeline
Implementation
Innovation & Challenges
Tasks Completed
Testing
Reusability
Future Enhancements

## Slide 3
To develop a device which can stream audio from PC / Mobile to speakers.
The device should make use of Wi-Fi wireless protocol to stream data.
It should also be able to stream audio at a higher bitrate.
The device should be able to perform without any lags whatsoever.
Problem Statement
27th October, 2016

## Slide 4
Raspberry Pi 3/ Arduino (primarily testing)
Wireless router (primarily testing)
PC / Laptop / Mobile Device (programming and testing)
USB sound card (good quality)
Wires to connect (Power, LAN, Audio cable etc.)
C/C++11
RaspbianOS / Ubuntu (Server Side)
Power Sockets with Electric Supply!
Requirements
27th October, 2016

## Slide 5
Work Allocation
  Bharath:
    Sending data from Client side using WASAPI
    Initial Setup
  Diptesh and Vinod
    Trying multiple other available implementations which failed. (PiMusicBox, Mopidy Server, MPDroidServer, and SoundWire Server, paprefs in Ubuntu, SWYH in Windows, nAudio in Windows)
    Receiving data on Server side using ALSA driver in Ubuntu.
    Setup (configuring WiFi module on RPi to connect to local WiFi).
    Implementation 2 with Shairport - Sync
Timeline:
  Procurement and Setup - 1 Week
  Server Side setup – 2 weeks
  Client side Audio Streaming API – 2 Week
  Quality Control and Testing – few days
Work allocation & Timeline
27th October, 2016

## Slide 6
Implementation-1
Ragam Client
Wi-Fi Router
(Access Point for Internet)
Speakers
(Target)
Music Player
Sound Card
ALSA
Ragam Server
Raspbian/ Linux
WASAPI
Windows
TCP/IP
TCP/IP

## Slide 7
Implementation-2
Wi-Fi Router
(Access Point for Internet)
Speakers
(Target)
27th October, 2016
AirPlay Client
ShairPort
Sync
Raspbian/ Linux/ OpenWRT
Windows/ Mac / Android
Music Transmission with Time Stamp
ALSA
Music Transmission with Buffer

## Slide 8
We have used the Windows Audio Session API for capturing sound data from the output buffer.
This allows us to capture data, which is then transferred to Server Side or can be saved as a wave file.
Audio lag reduction, and underrun errors on Raspberry Pi while using ALSA API.
Buffer Allocation due to low memory of Raspberry Pi.
Understanding of WAS and ALSA API
27th October, 2016
Innovation & Challenges

## Slide 9
We can play low bitrate Audio at server side without any lag whatsoever (through iTunes).
We can play highest available bitrate Audio (ALAC) files also without any lag on the server side.
27th October, 2016
Tasks Completed - I

## Slide 10
Capturing audio on the client side using the WASAPI which can be written to a WAV file.
Socket connection establishing and sending data to Raspberry Pi.
Playing generic system audio on Raspberry Pi device with minimal lag (low latency).
In this case, we are capturing audio from sound card, so it doesn’t matter which audio player we use, this being a limitation of our previous implementation.
27th October, 2016
Tasks Completed - II

## Slide 11
User Experience
  Delay time
    Method - I
      Client Side (Windows PC) - > Server Side (RPi) - > Sepakers
    Method - II
      Client Side (Windows PC) - > Server Side (RPi) - > Sepakers
      Client Side (Android) - > Server Side (RPi) - > Sepakers
      Client Side (Apple Devices) - > Server Side (RPi) - > Sepakers
  Audio Quality
    Method - I
      Client Side (Windows PC) - > Server Side (RPi) - > Sepakers.
    Method - II
      Client Side (Windows PC) - > Server Side (RPi) - > Sepakers
      Client Side (Android) - > Server Side (RPi) - > Sepakers
      Client Side (Apple Devices) - > Server Side (RPi) - > Sepakers
Testing
27th October, 2016

## Slide 12
Shairport Sync is a open source library which creates a server on Raspberry Pi / Ubuntu / Debian / OpenWRT.
In WASAPI, We have tried to implement the code using functions which can be re-used.
We have mostly use the WASAPI, which supports function calling, and thus even our part of the code is reusable.
Our server side code for Implementation-II are C programs which can be run individually, and could also be called from crontab of the server during bootup.
Reusability
27th October, 2016

## Slide 13
Music Streaming to an FM frequency.
We need to have iTunes (or Airplay supportive client side), we could later obliterate this limitation if we implement an open source uPnP / BubblePnP Server.
Currently for implementation two, we can only use Windows, we will have to write the same OS level audio capturing for Linux.
  Most of the parameter in implementation are hard-coded due to time constraint, we could have a configuration file for them.
  Downsampling the file before sending data to server to reduce bandwidth.
  Supporting multiple audio format
27th October, 2016
Future Enhancements

## Slide 14
http://make.witworks.com/preorder/trippy [5th September 2016]
https://gramofon.com/ [15th September 2016]
https://www.bose.com/en_us/products/speakers/wireless_speakers/soundtouch-10-wireless-system.html [15th September 2016]
http://www.ebay.in/itm/Bose-Soundtouch-10-/272349437205
Google Images (Non – Copyright images like Clipart used from OpenClipart, and ClipartPanda)
https://msdn.microsoft.com/en-us/library/windows/desktop/dd371455(v=vs.85).aspx
http://alsa-project.org/main/index.php/Main_Page
References
14th September, 2016

## Slide 15
Thank you! 
Questions ?
27th October, 2016